REQUEST FOR QUOTATION

NR 3/2016

for the purchase of an automatic line for lamellar coatings with the use of solvent-based paints and watercolour using trays in a fire furnace to separate the assortment

| Name of the Ordering Party |  |
| --- | --- |

Gaweł Zakład Produkcji Śrub S. A.

Palikówka 198

36-073 Strażów

Tax ID No. (NIP): 5170282359

General Provisions

This proceeding takes place by way of a request for quotation under the principle of competitiveness, in relation to the execution of the project titled “Environment-friendly lamellar zinc coating technology – Green industry – Poland” in the scope of the Green Industry Innovation for Poland program.

Subject of Procurement

The subject of procurement is the Ordering Party’s purchase of an automatic line for lamellar coatings with the use of solvent-based paints and watercolour using trays in a fire furnace to separate the assortment.

Specification of the lamellar coatings line:

- Coatings machine (part I)

  - AUTOMATIC LOADING TO A FEEDING VIBRATOR WITH A MAXIMUM LOAD CAPACITY OF 1,500 KG AND ROTATION BY 180⁰ WITH A WEIGHTING SYSTEM ALLOWING UNIFORM LOADING TO VARNISH BASKETS WITH THE “END OF LOADING” FUNCTION

  - AUTOMATIC PLASTIC TRAY AT THE LOADING VIBRATOR PROVIDED FOR DELICATE LOADING OF VARNISH BASKETS

  - INTERCHANGEABLE CONTINUOUS TRANSPORT BETWEEN THE LOADED AND EMPTY BASKETS OF UNLOADED PAINTED ASSORTMENT

  - HIGH FLEXIBILITY OF DIVERSIFYING THE COATING APPLICATION PROCEDURE

- DIPPING (TIME, SPEED, MULTIPLICITY, DIRECTION OF ROTATION)

- CENTRIFUGATION (TIME, SPEED, MULTIPLICITY, DIRECTION OF ROTATION)

- OPTION (ABILITY) TO ROTATE THE BASKET BY 45⁰ - 85⁰ (TIME, SPEED, MULTIPLICITY, DIRECTION OF ROTATION)

  - QUICK TRANSPORT AND REPLACEMENT OF BASKETS FROM THE LADLE TO THE FURNACE TRAYS’ TIPPLER

  - UNLOADING OF PAINTED PRODUCTS FROM THE BASKET TO THE FURNACE TRAY WITH THE ABILITY OF ROTATE TO 180⁰ TO ENSURE THOROUGH REMOVAL OF THE PAINTED PRODUCTS FROM THE BASKETS

  - ABILITY TO LOAD HARDENED AND COOLED-OFF ASSORTMENT FROM THE TRAY

TO THE VARNISH BASKETS FOR REPEATED PAINTING IN CASE OF NECESSITY TO APPLY ANOTHER COATING, MONITORING SYSTEM

  - VARNISH LADLES WITH A SET OF PAINT MIXING PUMPS FROM THE LADLE’S BOTTOM, INCLUDING	A MOUNTED SIEVE WHICH PROTECTS THE PUMP FROM PENETRATION OF UNWANTED ELEMENTS WHICH MIGHT DAMAGE IT

  - SET OF VARNISH BASKETS APPROPRIATE FOR PRODUCTS WITH MIN. Ø3, M4 AND

TX10 HEADSETS

  - AIR-CONDITIONER MAINTAINING FIXED TEMPERATURE AND LOW HUMIDITY IN

THE VARNISH CHAMBER

- Additional options for the coating machine

  - BARCODE SCANNING FOR THE PURPOSE OF ADJUSTING THE CORRECT PAINTING

PARAMETERS TO THE PRODUCT’S TYPE

  - FUNCTION OF CENTRIFUGATION IN TILT WITH AN INSTALLED DISK LIFTED

ALONG WITH THE BASKET

  - SECOND UNIT FOR APPLYING COATING FOR THE PURPOSE OF ACCELERATING THE SECOND PAINT REFITTING

  - STATION FOR UNUSED BASKETS IN THE CASE OF A SECOND PAINTING UNIT

REFITTING ACCELERATION

3. Coating hardening furnace (part II)

  - ELECTRICAL TRAY FURNACE, WHERE GIVEN TRAYS FOR PARTICULAR ZONES ARE PUSHED ONE AFTER ANOTHER AND AT THE END THE OUTGOING TRAY IS EXTRACTED AND TRANSPORTED USING AN LIFT/JACK TO THE TOP COOLING ZONE

  - ADJUSTABLE TRAY FEED SPEED

  - FURNACE ZONES:

    - DRYING – SOLVENT VAPORISATION AND EXTRACTION VIA THE VENTILATION SYSTEM, ROTATION REGULATOR

    - HARDENING – ASSORTMENT HEATING-UP AND MAINTENANCE OF FIXED TEMPERATURE, USE OF CIRCULAR DUCT FANS, ABILITY TO OBTAIN 300⁰C FOR THE PURPOSE OF COATING HARDENING, AIR EXTRACTION VIA THE VENTILATION SYSTEM

    - COOLING – ABILITY TO COOL THE AIR FROM THE OUTSIDE, ROTATION REGULATOR

  - TEMPERATURE RECORDER/ THERMOCOUPLE FOR THE COOLED-OFF ASSORTMENT, PROVIDING PROTECTION AGAINST REACHING THE CRITICAL DEW POINT AND ALLOWING APPLICATION OF THE NEXT COATING (DIFFERENCE BETWEEN THE PAINT TEMPERATURE AND THE PRODUCT TEMPERATURE). PRODUCT TEMPERATURE OF 20⁰C

- System for the supervision of the course of the coating application process and monitoring of the positions of given trays with the specified assortment (part III)

- Extraction hood with a gas concentration detector, including anti-explosion protection (part IV)

  - VARNISH CHAMBER EXTRACTION HOOD

  - UNLOADING ZONE IN FRONT OF THE FURNACE

5.3 EXTRACTOR FROM PARTICULAR FURNACE ZONES

- Catalytic converter (part V)

INTENDED PURPOSE: AIR PURIFICATION FROM VOLATILE ORGANIC COMPOUNDS GENERATED DURING THE COATING APPLICATION PROCESS, ALL HOOD EXTRACTIONS FROM THE MACHINE (VARNISH CHAMBER, TIPPLER IN FRONT OF THE FURNACE, PARTICULAR ZONES OF THE COATING HARDENING FURNACE)

Time of Procurement Execution

- Time of procurement execution: 20 weeks from the date of conclusion of agreement with the selected Contractor

- The Ordering Party restricts the right to change the time of the procurement subject’s execution. The new times will be agreed by way of consulting with the selected Contractor.

Place of Procurement Execution

  - Place of procurement execution: company registered seat and GZPŚ S.A. branch offices.

  - The Contractor must be able to execute the procurement embraced by the request for quotation at the area indicated in point 1.

Information regarding the legal, economic, financial and technical nature

  - The procurement is awarded by way of a request for quotation under the principle of competitiveness.

  - Submission of quotation does not result in any obligations towards the parties. Quotations are developed at the cost of the Contractors. Each Contractor may only submit a single quotation.

  - The following Contractors may apply for being awarded with the procurement:

      - List of companies that have incorporated the products (reference letters)

      - Declaration of good financial standing (company not in bankruptcy, etc.)

The above conditions shall be verified based on the Contractor’s declaration constituting appendix no. 2 to the request for quotation

  - Contractors associated with the Ordering Party in personal or capital terms are excluded from the proceeding for awarding the procurement. Personal or capital associations are understood as mutual relations between the Ordering Party or persons authorised to incur liabilities on behalf of the Ordering Party or persons acting on behalf of the Ordering Party in terms of preparation and execution of the proceeding of selecting the Contractor and the Contractor, especially based on:

- participation in the company as a partner in a private partnership or partnership;

- possession of at least 10% of the shares or stocks;

- acting as a member of a supervising or managing body, proxy, attorney;

- being in a matrimony, direct or secondary blood relation or kinship up to the second degree, relationship of adoption, guardianship or custody.

  - The Contractor is obliged to enclose to the quotation a declaration on the lack of the aforementioned associations in accordance with the form constituting Appendix no. 3 to this request for quotation.

  - The Ordering Party shall assess the fulfilment of the conditions for participation in the proceeding by using the fulfilled – not fulfilled criterion, i.e. whether or not the documents have been enclosed to the quotation and whether or not they fulfil the requirements specified in the request for quotation. Lack of any of the required declarations or documents or their enclosure in an incorrect form or in discordance with the requirements specified in the request for quotation shall result in rejection of the Contractor’s quotation, except for personal or capital relations between the Contractor and the Ordering Party, when the Contractor shall be excluded from participation in the proceeding.

  - The Ordering Party restricts the right to make any amendments in the conditions of the request for quotation in justified cases, and to cancel or conclude the proceeding without selecting any of the quotations, especially if the value of the quotation exceeds the resources allocated by the Ordering Party for financing the procurement.

| Description of the method of quotation price estimation |  |
| --- | --- |

- The Ordering Party accepts the submission of partial quotations and partial selection.

- The Contractor is obliged to specify the price for the execution of the subject of procurement in accordance with the quotation form. When submitting a quotation for one of the parts of the subject of procurement (partial quotation), the Contractor shall specify the price for the execution of the quoted part of the subject of procurement. The lines specifying the part of the subject of procurement not quoted by the Contractor shall be designated as “not applicable” or “-”

- The price specified in the quotation must be expressed in PLN or in EURO. The price must embrace all requirements of this request for quotation and all costs related to the duly and correct execution of the subject of procurement and the guidelines specified by the Ordering Party, related to the subject of procurement.

- If the price is provided in EURO, it shall be converted to PLN according to the average exchange rate of the National Bank of Poland applicable as of the date of publication of the request on the Ordering Party’s website.

- The price for the subject of procurement must be specified precisely; no variants in the price are allowed. All discounts or deductions should be included in the price estimation, so that the estimated price for the execution of the subject of procurement is the final price, without the need for the Ordering Party to make any conversions and other activities aimed at determining the price.

- The quotation price is the net price for the execution of the subject of procurement. Due to the possibility of submitting partial quotations, the Ordering Party shall separate study the net price for particular parts of the subject of procurement.

| Description of criteria to be followed by the Ordering Party during selection of the quotation, including specification of the meaning of those criteria and the method of quotation assessment |  |
| --- | --- |

- Quotation assessment criteria: price - 100 % (for each part of the subject of procurement, separately)

- Method of quotation assessment:

The “price criterion” – each Contractor shall be awarded with points for the net price of the subject of procurement, in the scale of 1:100, estimated acc. to the following formula:

lowest quoted net price

C= --------------------------------------------------------x 100 points.

net price of studied quotation

- The Ordering Party shall award the procurement to the Contractor, the quotation of which fulfils all requirements included in the request for quotation and shall be assessed in the specified criterion of choice as the most beneficial – by being awarded with the highest number of points (maximum of 100 points).

- If the selected Contractor refuses to conclude the agreement, the Ordering Party can conclude the agreement with the Contractor that fulfils the requirements of the request for quotation and the quotation of which was awarded with the highest amount of points, respectively.

- If the Ordering Party is not able to choose the most beneficial quotation due to the fact that more than one quotation was awarded with the same amount of points, the Ordering Party shall summon the Contractor that submitted the given quotations to submit additional quotations within the time specified by the Ordering Party. When submitting the additional quotations, the Contractors cannot quote prices higher than the prices quoted in the submitted quotations.

- If the most beneficial quotation is valued higher than the budget of the project for the execution of the task constituting the subject of quotation, the Ordering Party restricts the right to negotiate the quotation price with the Contractor, the price quotation of which was the most beneficial.

| Method of quotation development |  |
| --- | --- |

- The quotation must be developed on the “Quotation form” print constituting Appendix no. 1 to this request for quotation, in the Polish or English language, in a written and legible form, with indelible ink or pen, by print or on a computer. The quotation should be signed by the Contractor or the person authorised to represent the Contractor.

- The Quotation form constituting Appendix no. 1 to the request for quotation should include the following items:

- Declaration that the Contractor has fulfilled the conditions for participation in the proceeding, specified in paragraph 6 (3) of the request for quotation, constituting Appendix no. 2 to the request for quotation.

- Declaration on the lack of personal or capital associations between the Contractor and the Ordering Party constituting Appendix no. 3 to the request for quotation.

- The Contractor is bound by the submitted quotation for a period of 30 days starting after the expiry of the time of submission of quotations.

| Place and time of quotation submission, contact person |  |
| --- | --- |

- A quotation compliant with the enclosed form and this request for quotation must be submitted until 20.06.2016 r.

- Quotations submitted after this time shall not be taken into consideration.

- Quotations must be submitted in person or via mail (date of receipt is binding) to the following address:

Gaweł Zakład Produkcji Śrub S.A, Palikówka 198, 36-073 Strażów, Poland or via e-mail anna.dynowska@gzps.pl

- Person for contact with the Contractors: Anna Cynarska-Dynowska

- Statements, applications, notifications and information submitted between the Ordering Party and the Contractor shall be made in writing. The Ordering Party accepts the submission of documents and information in an electronic form to the following address: anna.dynowska@gzps.pl

- The request for quotation is available for download on the website

| List of appendices |  |
| --- | --- |

- Appendix no. 1 - Quotation form;

- Appendix no. 2 - Declaration on fulfilment of the conditions for participation in the proceeding;

- Appendix no. 3 - Declaration on the lack of personal or capital associations between the Contractor and the Ordering Party.

Appendix no. 1 – Quotation form

……………………………….					………………………………..

Contractor seal						       Place, date

QUOTATION

Contractor details

Name and surname/Name ……………………………………………

Address ………………………………………………………………

Tax ID no. (NIP) ………………………… REGON no. …………………………….

KRS no. ……………………………………………………………

Tel./Fax. ……………………………………………………………

E-mail address ………………………………………………………

In response to the request for quotation of  ……………………………….. we present the following price quotation:

| Description | Net value | VAT rate | Gross value |
| --- | --- | --- | --- |
| Coatings machine (part I) |  |  |  |
| Coating hardening furnace (part II) |  |  |  |
| System for the supervision of the course of the coating application process and monitoring of the positions of given trays with the specified assortment (part III) |  |  |  |
| Extraction hood with a gas concentration detector, including anti-explosion protection (part IV) |  |  |  |
| Catalytic converter (part V) |  |  |  |
| Total: |  |  |  |

I/we hereby declare that I am/we are acquainted with the conditions of the request for quotation and I/we do not raise any restrictions and that I/we obtained the necessary information and clarifications to develop the quotation.

I/we hereby declare that I am/we are bound by the quotation for the period of ………………………… calendar days starting from the expiry of the time for submitting quotations.

I/we hereby declare that if the Ordering Party chooses this quotation I am/we are obliged to conclude the agreement in the time and place specified by the Ordering Party.

………………………………

(Contractor signature and seal)

Appendix no. 2 – Declaration on fulfilment of the conditions for participation in the proceeding

……………………………….					………………………………..

Contractor seal				                         Place and date

Declaration

In relation to the request for quotation of ……………………………………………………………

I, hereby undersigned ……………………………………………………………………………………….

(name and surname of the person authorised to represent the Contractor)

acting for and on behalf of:

……………………………………………………………………………………………………………

(Contractor details – company full name and address)

hereby declare that:

- ……………………………………………………………………………………………………….

………………………………

(Contractor signature and seal)

Appendix no. 3 – Declaration on the lack of personal or capital associations between the Contractor and the Ordering Party

……………………………….					………………………………..

Contractor seal							Place and date

Declaration

In relation to the request for quotation of ……………………………………………………………

I, hereby undersigned ……………………………………………………………………………………….

(name and surname of the person authorised to represent the Contractor)

acting for and on behalf of:

……………………………………………………………………………………………………………

(Contractor details – company full name and address)

hereby declare that:

the Contractor is not associated in person or capital with the Ordering Party, i.e. there are no capital or personal relations within the meaning of mutual relations between the Ordering Party or persons authorised to incur liabilities on behalf of the Ordering Party or persons acting on behalf of the Ordering Party in terms of preparation and execution of the proceeding of selecting the Contractor and the Contractor, especially based on:

- participation in the company as a partner in a private partnership or partnership;

- possession of at least 10% of the shares or stocks;

- acting as a member of a supervising or managing body, proxy, attorney;

- being in a matrimony, direct or secondary blood relation or kinship up to the second degree, relationship of adoption, guardianship or custody.

……………………………….

(Contractor signature and seal)